        IBM
        ASSIGNMENT 1
        TEAM ID : PNT2022TMID08320
        TEAM LEAD : Laxmi Narayanan M (810419104056)
        EMAIL ID : laxminarayananmani@gmail.com

Source code :

#include<Servo.h>
int output1value= 0;
int sen1value= 0;
int sen2value= 0;
int const gas_sensor= A1;
int const LDR= A0;
int limit= 400;
long readU1trasonicDistance(int triggerpin, int echopin)\
{
 pinMode(triggerpin, OUTPUT); // clear the trigger
 digitalWrite(triggerpin, LOW);
 delayMicroseconds(2);
//sets the trigger pin to high state for 10 microseconds
 digitalWrite(triggerpin, HIGH);
 delayMicroseconds(10);
 pinMode(echopin, INPUT);
// reads the echo pin, and return the sound wave travel time
  return pulseIn(echopin, HIGH);
}
Servo servo_7;
void setup()
{
   Serial.begin(9600); //initialiize serial communication
  pinMode (A7, INPUT); //LDR
  pinMode (A1, INPUT); //gas sensor
  pinMode(13, OUTPUT); //connected to relay
  servo_7.attach(7, 500, 2500); //Green LED
  pinMode(8, OUTPUT); //signal to piezo burger
  pinMode(9, INPUT); //signal to PIR
  pinMode(10, OUTPUT); //signal to nPn as switch
  pinMode(4, OUTPUT); //Red LED
  pinMode(3, OUTPUT); //Green LED
}
void loop()
{
 //-------light intensity control--------//
//------------------------------------------------------------------------------
   int vall= analogRead(LDR);
  if (vall > 500)
 {
     digitalWrite(13, LOW);
 Serial.print("Bulb ON = ");
 Serial.print(vall);
 }
else
{
     digitalWrite(13, HIGH);
  Serial.print("Bulb OFF= ");
 Serial.print(vall);
 }
//-----------------------------------------------------------------------------
        //--------Light & fan control-------------//
//---------------------------------------------------------------------------------
   sen2value = digitalRead(9);
   if (sen2value==0)
   {
      digitalWrite(10, LOW); //nPn as switch OFF
      digitalWrite(4, HIGH); //Red lED ON, indicating no motion
      digitalWrite(3, HIGH); //Green LED OFF, since no motion
   Serial.print(" || NO Motion Detected ");
   }
if (sen2value== 1)
  {
      digitalWrite(10,	HIGH); // npn as swtich ON
    delay(5000);
        digitalWrite(4,LOW); //RED LED OFF
        digitalWrite(3,HIGH); //GREEN LED ON , indicatimg motion
    Serial.print(" ||Motion Detected! ");
   }
 //-------------------------------------------------------------------------------------------------
        //-------------Gas Sensor -----//
//--------------------------------------------------------------------------------------
 int val= analogRead(gas_sensor); //read sensor value
    Serial.print(" || Gas Sensor Value =");
    Serial.print(val); // printing in serial motion
//val =map(val, 300, 750, 0, 100);
  if(val > limit)
    {
        tone(8, 650);
    }
    delay(300);
    noTone(8);
 //-------------------------------------------------------------------------------------
        //--------servo motor -----//
 //-------------------------------------------------------------------------------------------
  sen1value = 0.01723 * readU1trasonicDistance(6, 6);
  if (sen1value < 100)
      {
        servo_7.write(90);
     Serial.print(" || Door Open! ; Distance = ");
     Serial.print(sen1value);
    Serial.print("\n");
}
 else
{
     servo_7.write(0);
     Serial.print(" || Door Closed! ; Distance = ");
     Serial.print(sen1value);
    Serial.print("\n");
}
delay(10);
}

CIRCUIT DIAGRAM :